AH-H003BF

19*4in1 15w zoom beam

User manual

Please read the instructions carefully before use

TABLE OF CONTENTS

1. Safety Instructions	2

2. Technical Specifications	4

3. How To Control  The Unit	5

4. shape	11

5. Trouble shooting	13

6. Fixture Cleaning	14

statement

The  product  has  well  capability  and  intact  packing  when  leave  factory. All  of  the  user should comply with warning item and manual, any misuse cause of the damages are not  included  in  our  guarantee,  and  also  can  not  be  responsible  for  any  malfunction  & problem owing to ignore the manual.

# 1. Safety Instructions

Please keep this User Guide for future consultation. If you sell the unit to another user, be sure that they also receive this instruction booklet.

 Unpack and check carefully there is no transportation damage before using the unit.

 Before  operating,  ensure  that  the  voltage  and  frequency  of  power  supply  match  the power requirements of the unit.

 It’s  important  to  ground  the  yellow/green  conductor  to  earth  in  order  to  avoid  electric shock.

 The unit is for indoor use only. Use only in a dry location.

 The  unit  must  be  installed  in  a  location  with  adequate  ventilation,  at  least  50cm  from adjacent surfaces. Be sure that no ventilation slots are blocked.

 Disconnect main power before replacement or servicing.

 Make sure there are no flammable materials close to the unit while operating as it is fire hazard.

 Use safety cable when fixes this unit. DO NOT handle the unit by taking its head only, but always by taking its base.

 Maximum ambient temperature is Ta: 40℃. DO NOT operate it where the temperature is higher than this Unit surface temperature may reach up to 85℃. DO NOT touch the housing bare-hand during its operation. Turn off the power and allow about 15 minutes for the unit to cool down before replacing or serving.

 In the event of serious operating problem, stop using the unit immediately.Never try to repair the unit by yourself. Repairs carried out by unskilled people can lead to damage or malfunction. Please contact the nearest authorized technical assistance center. Always use the same type spare parts.

 DO NOT touch any wire during operation as high voltage might be causing electric shock.

Warning:

 To prevent or reduce the risk of electrical shock or fire, do not expose the unit to rain or moisture.

 DO NOT open the unit within five minutes after switching off.

 The  housing,  the  lenses,  or  the  ultraviolet  filter  must  be  replaced  if  they  are  visibly damaged.

Caution:

There are no user serviceable parts inside the unit. DO NOT open the housing or attempt any repairs yourself. In the unlikely event your unit may require service, please contact your nearest dealer.

Installation:

The unit should be mounted via its screw holes on the bracket. Always ensure that the unit is  firmly  fixed  to  avoid  vibration  and  slipping  while  operating.  And  make  sure  that  the structure to which you are attaching the unit is secure and is able to support a weight of 10 times of the unit’s weight. Also always use a safety cable that can hold 12 times of the weight of the unit when installing the fixture.

The equipment must be fixed by professionals. And it must be fixed at a place where is out of the touch of people.

# 2. Technical Specifications

Light Sources: 19 x 15W  4in1  RGBW LED
Beam Angle: 7°~ 60°
Power Consumption: 300W
Power Voltage: AC 100-240V, 50/60Hz
Dimension: 33*23*37 cm
Packing Dimension: 410x330x490mm
Net Weight: 10Kgs
Gross Weight: 12Kgs

Control 
DMX Channel: 20/28 Channel
Control Modes: DMX, 
Software Upgrade: Firmware update via DMX link 
Pan/Tilt 
Pan/Tilt: 540°/ 220°
Pan/Tilt Resolution: 16 bit
Construction 
Display: LCD Display
Data In/Out socket: 3-pin & 5-pin XLR sockets
Power Socket: Powercon in/out
Protection Rating: IP20

Features 
Motorized liner zoom system, zoom range: 7°~60° 
Outstanding color macro effect 
Dimmer: 0~100% smooth dimming 
Variable strobe effects 
Fast, quiet operation and flicker free

# 3. How To Control  The Unit

The DMX512 is widely used in intelligent lighting control,with a DMX 512 controller.connect several lights together,dmx in and dmx out,

3 pin XLR connectors: Pin 1: GND, Pin 2: Negative signal (-), Pin 3: Positive signal (+)

Display:

MENU	To select the programming functions

DOWN	To go backward in the selected functions

uP	To go forward in the selected functions

ENTER	To confirm the selected functions

Set DMX Address Code

1	Press "Menu" to "Set DMX Address",and press"ENTER" keys to enter into

2	Show "Set DMX Address DMX Address:001",Press the "UP and DOWN"

keys to amended

- Press "ENTER"keys to save and Exit,Press the"MENU"Keys does not save and Exit

| function | Address CH Value Set to Slave Auto program Music control | Address001~XXX PAN…… Slave Master-Auto / Alone-Auto Master-Music / Alone-Music | Change address Show each channel value Slave receive position select auto run mode Sound auto run |
| --- | --- | --- | --- |
| info | Temp Inf | Head Temperature | XXX℃/℉ | current temperature |
|  | Soft Inf | xxx…… | software version |
| Person | Status | Pan Rev Tilt Rev P-Degree M Speed Mic Sens | ON/OFF ON/OFF 540/360 Speed 1~ 2 0~99% | Pan scan opposition title scan opposition scan angle select scan mode select mic sensitivity |
|  | Temp C/F | C/F switch | Temp unit switch |
|  | Reset Default | ON/OFF | Re-load all delivery parameter |
| Reset | Reset All |  | Reset the light |
| Adjust | CaliT CH | Password PAN TILT | Password=XXX PAN=XXX TILT | channels’ data calibrate code :050 PAN channel data calibrate TILT channel data calibrate |
| mode set | Standard Zone |  | Standard Channel mode Zone channel mode |

DMX channel´s functions and values (20/28 DMX channels):

| Mode/Channel | Value | Function |
| --- | --- | --- |
| Standard | Shape |  |  |
| 1 | 1 |  | PAN Movement 8bit : |
|  |  | 0-255 | Pan Movement |
| 2 | 2 |  | Pan Fine 16bit |
|  |  | 0-255 | Fine control of Pan movement |
| 3 | 3 |  | TILT Movement 8bit : |
|  |  | 0-255 | Tilt Movement |
| 4 | 4 |  | Tilt Fine 16bit |
|  |  | 0-255 | Fine control of Tilt movement |
| 5 | 5 |  | Speed Pan/Tilt movement: |
|  |  | 0-225 | max to min speed |
|  |  | 226-255 | no function |
| 6 | 6 |  | STROBE |
|  |  | 0-255 | Strobe from slow to fast |
| 7 | 7 |  | Dimmer intensity: |
|  |  | 0-255 | Intensity 0 to 100% |
| 8 | 8 |  | Dimmier mode |
|  |  | 0-49 | Dimmer mode 1 |
|  |  | 50-99 | Dimmer mode 2 |
|  |  | 100-149 | Dimmer mode 3 |
|  |  | 150-255 | Dimmer mode 4 |
| 9 | 9 |  | Zoom : |
|  |  | 0-255 | Zoom adjustment |
| 10 |  |  | Red LED -all arrays : |
|  |  | 0-255 | Red ( 0-Black , 255-100% Red ) |
| 11 |  |  | Green LED-all arrays : |
|  |  | 0-255 | Green ( 0-Black , 255-100% Green ) |
| 12 |  |  | Blue LED -all arrays : |
|  |  | 0-255 | Blue ( 0-Black , 255-100% Blue ) |
| 13 |  |  | White LED -all arrays : |
|  |  | 0-255 | White ( 0-Black , 255-100% White ) |
|  | 10 |  | Red LED -array 1 : |
|  |  | 0-255 | Red ( 0-Black , 255-100% Red ) |
|  | 11 |  | Green LED-array 1 : |
|  |  | 0-255 | Green ( 0-Black , 255-100% Green ) |
|  | 12 |  | Blue LED -array 1 : |
|  |  | 0-255 | Blue ( 0-Black , 255-100% Blue ) |
|  | 13 |  | White LED -array 1 : |
|  |  | 0-255 | White ( 0-Black , 255-100% White ) |
|  | 14 |  | Red LED -array 2 : |
|  |  | 0-255 | Red ( 0-Black , 255-100% Red ) |
|  | 15 |  | Green LED-array 2 : |
|  |  | 0-255 | Green ( 0-Black , 255-100% Green ) |
|  | 16 |  | Blue LED -array 2 : |
|  |  | 0-255 | Blue ( 0-Black , 255-100% Blue ) |
|  | 17 |  | White LED -array 2 : |
|  |  | 0-255 | White ( 0-Black , 255-100% White ) |
|  | 18 |  | Red LED -array 3 : |
|  |  | 0-255 | Red ( 0-Black , 255-100% Red ) |
|  | 19 |  | Green LED-array 3 : |
|  |  | 0-255 | Green ( 0-Black , 255-100% Green ) |
|  | 20 |  | Blue LED -array 3 : |
|  |  | 0-255 | Blue ( 0-Black , 255-100% Blue ) |
|  | 21 |  | White LED -array 3: |
|  |  | 0-255 | White ( 0-Black , 255-100% White ) |
| 14 | 22 |  | Rainbow: |
|  |  | 0-4 | No function |
|  |  | 5-29 | R |
|  |  | 30-54 | G |
|  |  | 55-79 | B |
|  |  | 80-104 | W |
|  |  | 105-129 | Rainbow colours 1 |
|  |  | 130-154 | Rainbow colours 2 |
|  |  | 155-174 | Rainbow colours 3 |
|  |  | 175-179 | Rainbow colours 4 |
|  |  | 180-184 | Rainbow colours 5 |
|  |  | 185-189 | Rainbow colours 6 |
|  |  | 190-210 | Rainbow colours 7 |
|  |  | 211-255 | Crossfading colours from slow to fast |
| 15 | 23 |  | Color Presets: |
|  |  | 0-4 | No function |
|  |  | 5--9 | White1 |
|  |  | 10--14 | White2 |
|  |  | 15-19 | White3 |
|  |  | 20-24 | White4 |
|  |  | 25-29 | White5 |
|  |  | 30-34 | White6 |
|  |  | 35-39 | Red |
|  |  | 40-44 | Green |
|  |  | 45-49 | Blue |
|  |  | 50-54 | Natural White |
|  |  | 55-59 | Full White |
|  |  | 60-64 | Yellow |
|  |  | 65-69 | Magenta |
|  |  | 70-74 | Cyan |
|  |  | 75-79 | Salmon |
|  |  | 80-84 | Turquoise |
|  |  | 85-89 | Light Green |
|  |  | 90-94 | Steel Blue |
|  |  | 95-99 | Orange |
|  |  | 100-104 | Straw |
|  |  | 105-109 | Pale Lavander |
|  |  | 110-114 | Pink |
|  |  | 115-119 | RED/WHITE |
|  |  | 120-124 | GREEN/RED |
|  |  | 125-129 | BLUE/GREEN |
|  |  | 130-134 | WHITE/RED |
|  |  | 135-139 | GREEN/PINK |
|  |  | 140-144 | RED/TURQUOISE |
|  |  | 145-149 | RED/WHITE/BLUE |
|  |  | 150-255 | Reserved |
| 16 | 24 |  | Color Presets Dimmer: |
|  |  | 0-255 | Dimmer 100 to 0% |
| 17 | 25 |  | Chase Patterns: |
|  |  | 1--14 | Led trun off |
|  |  | 15-30 | Chase 1 |
|  |  | 31-46 | Chase 2 |
|  |  | 47-62 | Chase 3 |
|  |  | 63-78 | Chase 4 |
|  |  | 79-94 | Chase 5 |
|  |  | 95-110 | Chase 6 |
|  |  | 111-126 | Chase 7 |
|  |  | 127-142 | Chase 8 |
|  |  | 143-158 | Chase 9 |
|  |  | 159-174 | Chase 10 |
|  |  | 175-190 | Chase 11 |
|  |  | 191-206 | Chase 12 |
|  |  | 207-222 | Chase 13 |
|  |  | 223-238 | Chase 14 |
|  |  | 239-255 | Chase 15 |
| 18 | 26 |  | Chase Speed: |
|  |  | 0-125 | Fast to Slow Backward |
|  |  | 126-130 | Stop(Speed=0) |
|  |  | 131-255 | Slow to Fast Forward |
| 19 | 27 |  | Chase Fade: |
|  |  | 0-255 | Fade Chase |
| 20 | 28 |  | Lamp on/off, reset, internal programs: |
|  |  | 0-79 | Normal |
|  |  | 80-99 | All motor reset |
|  |  | 100-255 | Normal |

# 4. shape

# 5. Trouble shooting

Following are a few common problems that may occur during operation. Here are some suggestions for easy troubleshooting:

A. The unit does not work, no light and the fan does not work

1. Check the connection of power and main fuse.

2. Measure the mains voltage on the main connector.

3. Check the power on LED.

B. Not responding to DMX controller

1. DMX LED should be on. If not, check DMX connectors, cables to see if link properly.

2. If the DMX LED is on and no response to the channel, check the address settings and DMX polarity.

3. If you have intermittent DMX signal problems, check the pins on connectors or on

PCB of the unit or the previous one.

4. Try to use another DMX controller.

5. Check if the DMX cables run near or run alongside to high voltage cables that may cause damage or interference to DMX interface circuit.

C. One of the channels is not working well

1. The stepper motor might be damaged or the cable connected to the PCB is broken.

2. The motor’s drive IC on the PCB might be out of condition.

# 6. Fixture Cleaning

The cleaning of internal and external optical lenses and/or mirrors must be carried out periodically to optimize light output. Cleaning frequency depends on the environment in which the fixture operates: damp, smoky or particularly dirty surrounding can cause greater accumulation of dirt on the unit’s optics.

 Clean with soft cloth using normal glass cleaning fluid.

 Always dry the parts carefully.

 Clean the external optics at least every 20 days. Clean the internal optics at least every 30/60 days.