36pcs LED Moving Head Wash Light

Product Model:LH-C014C,LH-C014D
Product Parameters:
Power consumption:450W(12W LED)/540W(18W LED)
Light source:36pcs*12W/15W LED (optional)
Color:RGBW 4in1/RGBWA+UV 6in1(optional)

Voltage: AC90-260V 50/60Hz

Consumption:450W(12W LED)/540W(15W LED)
LEDs:Light source:36pcs*12W/15W LED (optional)
Color:RGBW 4in1/RGBWA+UV 6in1(optional)
About 6,000 Hours working time
Zoom angle:10---60 degree
Shutter: Pulse effect; random strobe slow to fast
Dimming: 0% - 100%
Built-in programs with macro effects
Pan: 540 degree (16 bit)
Tilt: 270°(16bit) 
DMX Channel : 16CH(RGBWA)/18CH(RGBWA+UV) 
Control Mode : DMX, Sound Active , Auto , Master-Slave
Big LCD Touch screen 
3 pin XLR DMX In/Out
Powercon In 
Appearance: Black/White housing optional 
Heat resisting ABS material 
CE (LVD , EMC ) and RoHS
IP Rate : IP 20 
Net weight :10 kg 
Carton packing size: 36*39*49 cm(1pc / CTN ),G.W.:12kg
Flycase size:55*41.5*55cm (2pcs / CTN ),G.W.:38KG
             78*54*75cm (4pcs / CTN ),G.W.:72.5KG