44-10W outdoor led bar user manual

- Graphic parts：

E

A．Function Keys

B．Plus key

C．Minus key

D．Enter Key

E．LCD display window

A    B    C   D

Operating instructions:Press A to cycle out of eight different functional effect,the first two digits on the digital tube represents the current function(According to the function table).After two figures represent the kinds of this function parameters including address code and speed. Press keys B or C to modify the parameter value.Press D button to confirm.

LCD Display Window Function Table，（All functions selected and then press the D key to confirm）

| No. | Display | Function menu |
| --- | --- | --- |
| 1 | DMX-8CH D: 001 | Channel address code，（001—512） B、C key add and subtract address code value |
| 2 | DMX-CH D: 4CH | Channel selection，（8CH/4CH） B、C key plus or minus the number of channels |
| 3 | Jump D: 099 | Jumping（0-99） B, C key to modify speed |
| 4 | Gradient D: 099 | Gradient（0-99） B、C key to modify speed |
| 5 | Color R D: 255 | R color selection，（000—255） B, C key to modify color selection |
| 6 | Color G D: 255 | G color selection，（000—255） B、Ckey to modify color selection |
| 7 | Color B D: 255 | B color selection，（000—255） B、Ckey to modify color selection |
| 8 | Color W D: 255 | W color selection，（000—255） B、Ckey to modify color selection |

2.LCD Display the background comparison table, (long press A function key to enter in DMX mode, press D key to confirm after all functions are selected)

| NO. | Display | Function Description |
| --- | --- | --- |
| 1 | current R: 235 | R color current，（20—255） B, C key to modify the current |
| 2 | current G: 235 | Gcolor current，（20—255） B、C key to modify the current |
| 3 | current B: 235 | B color current，（20—255） B、C key to modify the current |
| 4 | current W: 235 | W color current，（20—255） B、C key to modify the current |
| 5 | LEDspeed D: 1 | Dimming speed，（000—255） B、C key to modify the dimming speed |
| 6 | oC D: 060 | Temperature setting，（040—070） B、C key to modify the temperature |
| 7 | FAN D: 001 | Fan mode setting， （000 Conventional fan） （001 Temperature control fan） B, C key modification |
| 8 | Model D: ****** | Program serial number |

3．DMX512  8 Channel description

| No. | Function | Description |
| --- | --- | --- |
| Channel 1 | Total dimming | total dimming, linear dimming, from dark to light |
| Channel 2 | Total Strobe | total strobe, from slow to fast |
| Channel 3 | Function selection | 0—50：nothing； 51—100：Jumping； 101—150：Gradient； 151—255：Pulse； |
| Channel 4 | Functional speed | Functional speed, from slow to fast |
| Channel 5 | R dimming | R dimming，linear dimming, from dark to light |
| Channel 6 | G dimming | G dimming，linear dimming, from dark to light |
| Channel 7 | B dimming | B dimming，linear dimming, from dark to light |
| Channel 8 | W dimming | W dimming，linear dimming, from dark to light |

4．DMX512  4 Channel description

| NO. | Function | Description |
| --- | --- | --- |
| Channel 1 | R dimming | R dimming，linear dimming, from dark to light |
| Channel 2 | G dimming | G dimming，linear dimming, from dark to light |
| Channel 3 | B dimming | B dimming，linear dimming, from dark to light |
| Channel 4 | W dimming | W dimming，linear dimming, from dark to light |

5．Features：

The operation is very simple, user-friendly design, dimming flicker-free and without jitter. Suitable for photography, TV stations and other places with strict lighting requirements