10R 260W BEAM MOVING HEAD

USER MANUAL

Please read over this manual before operating the light

# Chapter 1 Installation and attention

## 1.1 Maintenance

- To reduce the risk of electrical shock or fire, do not expose this unit to rain or moisture.

- Intermittently using will extend this item’s service life.

- Please clear the fan, fan net , and optical lens in order to keep good work state.

- Do not use the alcohol or any other organic solvent to wipe the shell.

## 1.2 Statement

The product has perfect performance and integrity packing. All users should be strictly complying with the warning and operating instructions as stated. Or we aren’t in charge of any result by misuse. Any damage resulting by misuse is not within the Company’s warranty. Any fault or problem caused by neglecting the manual is also not in the charge of dealers.

Note: All information is subject to change without prior notice.

## 1.3 Safety Precaution

- In order to guarantee the product’s life, please don’t put it in the damp places or even the environment over 60 degree.

- Always mount this unit in safe and stable matter.

- Install or dismantle should be operated by professional engineer.

- Using lamp，the change rate of power voltage should be within±10%. If the voltage is too high, it will shorten the light’s life; if it’s not enough, will influence the effect.

- Please restart it 20 minutes later after turning off the light, until full-cooling. Frequent switching will reduce the life span of lamps and bulbs; intermittent using will improve the life of bulbs and lights.

- In order to make sure the product is used correctly, please read the Manual carefully.

## 1.4 Product Instruction

- Lamp: Osram lamp burner 240W

- Channel mode: 18 DMX512 Channel

- Pan scan: 540°(16bit) Electric correction

- Tilt scan: 270° (16bit) Electric correction

- Amazing dot  matrix, four tact switch, 180° turning show

- Color wheel: 14colors + white, and seven color effect;

- Gobo wheel: 14 gobos(8 fixed gobos + 5 glass gobos + white);

- Effect Wheel: 8 prism/8+16prism;

- 0-100% mechanical dimming, mechanical dimming and free dimming available.

- Strobe macro control available;

- Lens optical system alchemical force , beam angle 0～4°;

- Over-heat protection

- Power Input: 100-240V, 50/60Hz

- Power Dissipation: 400W

- IP level :IP20

- Magnetic ballast and AC/Dc power supply

- Product Size：310×230×500mm

- Packing Size: 635X440X725

- Net weight：14.5KG

## 1.5  Cable connection（DMX）

Use a cable conforming to specifications EIA RS-485: 2-pole twisted, shielded, 120Ohm characteristic impedance, 22-24 AWG, low capacity. Do not use microphone cable or other cable with characteristics differing from those specified. The end connections must be made using XLR type 3 or 5-pin male/female connectors. A terminating plug must be inserted into the last projector with a resistance of 120Ohm (minimum 1/4 W) between terminals 2 and 3.

IMPORTANT: The wires must not make contact with each other or with the metal casing of the connectors. The casing itself must be connected to the shield braid and to pin 1 of the connectors.

Figure 1  DMX Cable connection

## 1.6 Rigging (Optional)

This equipment can be positioned and fixed by clamp in every direction of the stage. Locking system makes it easy to fasten to the bracket.

Attention! Two clamps are needed to fix the equipment. Every clamp is locked by fastener of 1/4 kind. Fastener can only be locked clockwise.

Attention! Fasten a safety string to the additional hole of side aluminum piece. The secondary accessory could not hang on the delivery handle. Nip the equipment on bracket.

- Check if rigging clamp (not including the one inside) damaged or not? If stand ten times weight as the equipment. Make sure the architecture can stand ten times weight as all the equipment, clamps, wirings and other additional fixtures.

- Screws for clamping must be fixed firmly. Take one M12 screw (Grade 8.8 or higher) to clamp bracket, and then screw the nuts.

- Level the two hanging points at the bottom of clamp. Insert fastener to the bottom, lock the two levers by 1/4 rotating clockwise; then install another clamp.

- Install on safety string which stands at least ten times weight as equipment. Terminal of the accessory is designed for clamps.

- Make sure pan/tilt lock unlocked or not. Keep the distance more than 1M from equipment to flammable material or lighting source.

Figure 2  Installation

# Chapter 2 Channel description

## 2.2  Channel Detail

| TOP | LEVEL 1 | LEVEL 2 | LEVEL 3 |
| --- | --- | --- | --- |
| DMX ADDRESS | 001-512 |  |  |
| LAMP | LAMP CONTROL | DO NOTHING AND EXIT/OPEN LAMP/CLOSE LAMP |  |
|  | POWER ON LAMP ON | ON/OFF |  |
|  | AFTER RESET LAMP ON | ON/OFF |  |
|  | LAMP BY DMX CONTROL | ON/OFF |  |
| SETTING | CHANNEL MODE | 18CH |  |
|  | PAN TILT FEEDBACK | ON/OFF |  |
|  | PAN INVERT | ON/OFF |  |
|  | TILT INVERT | ON/OFF |  |
|  | SWAP PAN TILT | ON/OFF |  |
|  | SOUND SENSITIVITY | 1-15-30 |  |
| DISPLAY | LANGUAGE | ENGLISH/中文 |  |
|  | DISPLAY INVERSE | YES/NO |  |
|  | BACKLIGHT | PERMANENTLY ON/30S OFF |  |
| MANUALLY CONTROL | PAN | 0-255 |  |
|  | PAN FINE | 0-255 |  |
|  | TILT | 0-255 |  |
|  | TILT FINE | 0-255 |  |
|  | PAN&TILE SPEED | 0-255 |  |
|  | STROBE | 0-255 |  |
|  | DIMMER | 0-255 |  |
|  | GOBO | 0-255 |  |
|  | COLOR | 0-255 |  |
|  | FOCUS | 0-255 |  |
|  | PRISM 1 | 0-255 |  |
|  | PRISM 1 ROTATE | 0-255 |  |
|  | PRISM 2 | 0-255 |  |
|  | PRISM 2 ROTATE | 0-255 |  |
|  | FROST | 0-255 |  |
|  | MULTICOLOR | 0-255 |  |
| AUTO MODE | MASTER AUTO RUN | RUNNING…* |  |
|  | ALONE AUTO RUN | RUNNING…* |  |
|  | MASTER SOUND RUN | RUNNING…* |  |
|  | ALONE SOUND RUN | RUNNING…* |  |
| FACTORY DEFAULT | YES/NO |  |  |
| INFORMATION | LAMP STATUS NOW | ON/OFF |  |
|  | SOFTWARE VERSION | Vx.x |  |
|  | RDM UID | xxx... |  |
|  | RESET INFO | X RASTER |  |
|  |  | Y RASTER |  |
|  |  | X HALL |  |
|  |  | Y HALL |  |
|  |  | FOCUS HALL |  |
|  |  | GOBO HALL |  |
|  |  | COLOR HALL |  |
| RESET | YES/NO |  |  |
| SEND PARAMETERS | YES/NO |  |  |

| 18CH | VALUE | FUNCTION |
| --- | --- | --- |
| CH1 | 0-255 | Pan |
| CH2 | 0-255 | Pan fine |
| CH3 | 0-255 | Tilt |
| CH4 | 0-255 | Tilt fine |
| CH5 | 0-255 | Pan/Tile speed(fast to slow) |
| CH6 | 0-255 | Dimmer 0-100% |
| CH7 | 0-5 | Shutter close |
|  | 6-20 | Shutter open |
|  | 21-70 | Normal synchronous strobe(slow to fast) |
|  | 71-100 | Not synchronous strobe(slow to fast) |
|  | 101-150 | Sinewave strobe(slow to fast) |
|  | 151-190 | Opening pulse strobe(slow to fast) |
|  | 191-230 | Closing pulse strobe(slow to fast) |
|  | 231-255 | Shutter open |
| CH8 | 0-10 | No effect |
|  | 11-255 | Frost 100% |
| CH9 | 0-5 | Open(white) |
|  | 6-10 | Open->Color 1 |
|  | 11-15 | Color 1 |
|  | 16-20 | Color 1->Color 2 |
|  | 21-25 | Color 2 |
|  | 26-30 | Color 2->Color 3 |
|  | 31-35 | Color 3 |
|  | 36-40 | Color 3->Color 4 |
|  | 41-45 | Color 4 |
|  | 46-50 | Color 4->Color 5 |
|  | 51-55 | Color 5 |
|  | 56-60 | Color 5->Color 6 |
|  | 61-65 | Color 6 |
|  | 66-70 | Color 6->Color 7 |
|  | 71-75 | Color 7 |
|  | 76-80 | Color 7->Color 8 |
|  | 81-85 | Color 8 |
|  | 86-90 | Color 8->Color 9 |
|  | 91-95 | Color 9 |
|  | 96-100 | Color 9->Color 10 |
|  | 101-105 | Color 10 |
|  | 106-110 | Color 10->Color 11 |
|  | 111-115 | Color 11 |
|  | 116-120 | Color 11->Color 12 |
|  | 121-125 | Color 12 |
|  | 126-130 | Color 12->Color 13 |
|  | 131-135 | Color 13 |
|  | 136-140 | Color 13->Color 14 |
|  | 141-145 | Color 14 |
|  | 146-150 | Color 14->Open |
|  | 151-200 | CW flow(slow to fast) |
|  | 201-205 | Color wheel stop |
|  | 206-255 | CCW flow(slow to fast) |
| CH10 | 0-5 | Open(white) |
|  | 6-10 | Gobo 1 |
|  | 11-15 | Gobo 2 |
|  | 16-20 | Gobo 3 |
|  | 21-25 | Gobo 4 |
|  | 26-30 | Gobo 5 |
|  | 31-35 | Gobo 6 |
|  | 36-40 | Gobo 7 |
|  | 41-45 | Gobo 8 |
|  | 46-50 | Gobo 9 |
|  | 51-55 | Gobo 10 |
|  | 56-60 | Gobo 11 |
|  | 61-65 | Gobo 12 |
|  | 66-70 | Gobo 13 |
|  | 71-90 | Gobo 14 |
|  | 91-97 | Gobo1 shake(slow to fast) |
|  | 98-104 | Gobo2 shake(slow to fast) |
|  | 105-111 | Gobo3 shake(slow to fast) |
|  | 112-118 | Gobo4 shake(slow to fast) |
|  | 119-125 | Gobo5 shake(slow to fast) |
|  | 126-132 | Gobo6 shake(slow to fast) |
|  | 133-139 | Gobo7 shake(slow to fast) |
|  | 140-146 | Gobo8 shake(slow to fast) |
|  | 147-153 | Gobo9 shake(slow to fast) |
|  | 154-160 | Gobo10 shake(slow to fast) |
|  | 161-167 | Gobo11 shake(slow to fast) |
|  | 168-174 | Gobo12 shake(slow to fast) |
|  | 175-181 | Gobo13 shake(slow to fast) |
|  | 182-188 | Gobo14 shake(slow to fast) |
|  | 189-195 | Gobo14 shake(slow to fast) |
|  | 196-202 | Gobo14 shake(slow to fast) |
|  | 203-209 | Gobo14 shake(slow to fast) |
|  | 210-230 | CW flow(slow to fast) |
|  | 231-234 | Gobo wheel stop |
|  | 235-255 | CCW flow(slow to fast) |
| CH11 | 0-120 | No effect |
|  | 121-255 | Color effect 100%(only valid when no frost) |
| CH12 | 0-10 | Prism 1 off |
|  | 11-255 | Prism 1 on |
| CH13 | 0-2 | Prism stop rotate |
|  | 3-150 | Prism angle 0-400 |
|  | 151-200 | Prism CW(slow to fast) |
|  | 201-205 | Prism stop rotate |
|  | 206-255 | Prism CCW(slow to fast) |
| CH14 | 0-10 | Prism 2 off |
|  | 11-255 | Prism 2 on |
| CH15 | 0-255 | Reserved |
| CH16 | 0-255 | Focus(From far to near) |
| CH17 | 0-99 | Not valid |
|  | 100-105 | Lamp off(at least5S) |
|  | 106-199 | Not valid |
|  | 200-205 | Lamp on(at least 5S) |
|  | 206-255 | Not valid |
| CH18 | 0-250 | Not valid |
|  | 251-255 | All motor reset(at least 5S) |

| 顶层菜单 | 第一级 | 第二级 | 第三级 |
| --- | --- | --- | --- |
| 地址码 | 001-512 |  |  |
| 灯泡 | 灯泡控制 | 无操作并退出/打开灯泡/关闭灯泡 |  |
|  | 开机亮灯 | 开/关 |  |
|  | 复完位亮灯 | 开/关 |  |
|  | 灯泡受DMX控制 | 开/关 |  |
| 参数设置 | 通道模式设置 | 18通道 |  |
|  | XY纠错启用 | 开/关 |  |
|  | X轴反向 | 开/关 |  |
|  | Y轴反向 | 开/关 |  |
|  | XY轴交换 | 开/关 |  |
|  | 声控灵敏感度 | 1-15-30(越大越灵敏) |  |
| 显示设置 | 语言 | ENGLISH/中文 |  |
|  | 显示反向 | 是/否 |  |
|  | 背光设置 | 常开/30秒关闭 |  |
| 手动控制 | X轴 | 0-255 |  |
|  | X轴微调 | 0-255 |  |
|  | Y轴 | 0-255 |  |
|  | Y轴微调 | 0-255 |  |
|  | XY轴速度 | 0-255 |  |
|  | 频闪 | 0-255 |  |
|  | 调光 | 0-255 |  |
|  | 图案 | 0-255 |  |
|  | 颜色 | 0-255 |  |
|  | 调焦 | 0-255 |  |
|  | 棱镜1 | 0-255 |  |
|  | 棱镜1自转 | 0-255 |  |
|  | 棱镜2 | 0-255 |  |
|  | 棱镜2自转 | 0-255 |  |
|  | 雾化切入 | 0-255 |  |
|  | 七彩切入 | 0-255 |  |
| 自走模式 | 主机内置自走 | 运行中...* |  |
|  | 单机内置自走 | 运行中...* |  |
|  | 主机声控自走 | 运行中...* |  |
|  | 单机声控自走 | 运行中...* |  |
| 恢复出厂设置 | 是/否 |  |  |
| 信息 | 当前灯泡状态 | 开/关 |  |
|  | 软件版本 | Vx.x |  |
|  | RDM UID码 | xxx... |  |
|  | 复位检测信息 | X轴光耦 |  |
|  |  | Y轴光耦 |  |
|  |  | X轴霍尔 |  |
|  |  | Y轴霍尔 |  |
|  |  | 调焦霍尔 |  |
|  |  | 图案霍尔 |  |
|  |  | 色盘霍尔 |  |
| 复位 | 是/否 |  |  |
| 发送本机参数 | 是/否 |  |  |

| 18通道 | 数值 | 功能 |
| --- | --- | --- |
| CH1 | 0-255 | 水平 |
| CH2 | 0-255 | 水平微调 |
| CH3 | 0-255 | 垂直 |
| CH4 | 0-255 | 垂直微调 |
| CH5 | 0-255 | 水平垂直速度，快到慢 |
| CH6 | 0-255 | 调光，0~100% |
| CH7 | 0-5 | 闭光 |
|  | 6-20 | 开光 |
|  | 21-70 | 同步频闪慢到快 |
|  | 71-100 | 异步频闪慢到快 |
|  | 101-150 | 渐开渐关慢到快 |
|  | 151-190 | 渐开快关慢到快 |
|  | 191-230 | 渐关快开慢到快 |
|  | 231-255 | 开光 |
| CH8 | 0-10 | 无雾化 |
|  | 11-255 | 雾化100% |
| CH9 | 0-5 | 无色盘 |
|  | 6-10 | 白光到色盘1 |
|  | 11-15 | 色盘1 |
|  | 16-20 | 色盘1到色盘2 |
|  | 21-25 | 色盘2 |
|  | 26-30 | 色盘2到色盘3 |
|  | 31-35 | 色盘3 |
|  | 36-40 | 色盘3到色盘4 |
|  | 41-45 | 色盘4 |
|  | 46-50 | 色盘4到色盘5 |
|  | 51-55 | 色盘5 |
|  | 56-60 | 色盘5到色盘6 |
|  | 61-65 | 色盘6 |
|  | 66-70 | 色盘6到色盘7 |
|  | 71-75 | 色盘7 |
|  | 76-80 | 色盘7到色盘8 |
|  | 81-85 | 色盘8 |
|  | 86-90 | 色盘8到色盘9 |
|  | 91-95 | 色盘9 |
|  | 96-100 | 色盘9到色盘10 |
|  | 101-105 | 色盘10 |
|  | 106-110 | 色盘10到色盘11 |
|  | 111-115 | 色盘11 |
|  | 116-120 | 色盘11到色盘12 |
|  | 121-125 | 色盘12 |
|  | 126-130 | 色盘12到色盘13 |
|  | 131-135 | 色盘13 |
|  | 136-140 | 色盘13到色盘14 |
|  | 141-145 | 色盘13 |
|  | 146-150 | 色盘14到白光 |
|  | 151-200 | 正转慢到快 |
|  | 201-205 | 停止 |
|  | 206-255 | 反转慢到快 |
| CH10 | 0-5 | 无图案 |
|  | 6-10 | 图案 1 |
|  | 11-15 | 图案 2 |
|  | 16-20 | 图案 3 |
|  | 21-25 | 图案 4 |
|  | 26-30 | 图案 5 |
|  | 31-35 | 图案 6 |
|  | 36-40 | 图案 7 |
|  | 41-45 | 图案 8 |
|  | 46-50 | 图案 9 |
|  | 51-55 | 图案 10 |
|  | 56-60 | 图案 11 |
|  | 61-65 | 图案 12 |
|  | 66-70 | 图案 13 |
|  | 71-90 | 图案 14 |
|  | 91-97 | 图案 1 抖动慢到快 |
|  | 98-104 | 图案 2 抖动慢到快 |
|  | 105-111 | 图案 3 抖动慢到快 |
|  | 112-118 | 图案 4 抖动慢到快 |
|  | 119-125 | 图案 5 抖动慢到快 |
|  | 126-132 | 图案 6 抖动慢到快 |
|  | 133-139 | 图案 7 抖动慢到快 |
|  | 140-146 | 图案 8 抖动慢到快 |
|  | 147-153 | 图案 9 抖动慢到快 |
|  | 154-160 | 图案 10 抖动慢到快 |
|  | 161-167 | 图案 11 抖动慢到快 |
|  | 168-174 | 图案 12 抖动慢到快 |
|  | 175-181 | 图案 13 抖动慢到快 |
|  | 182-188 | 图案 14 抖动慢到快 |
|  | 189-195 | 图案 14 抖动慢到快 |
|  | 196-202 | 图案 14 抖动慢到快 |
|  | 203-209 | 图案 14 抖动慢到快 |
|  | 210-230 | 正转慢到快 |
|  | 231-234 | 停止 |
|  | 235-255 | 反转慢到快 |
| CH11 | 0-120 | 无七彩 |
|  | 121-255 | 七彩100%（当有雾化时七彩无效） |
| CH12 | 0-10 | 无棱镜1 |
|  | 11-255 | 棱镜1切入 |
| CH13 | 0-2 | 棱镜自转停止 |
|  | 3-150 | 棱镜角度0-400度 |
|  | 151-200 | 棱镜正转慢到快 |
|  | 201-205 | 棱镜自转停止 |
|  | 206-255 | 棱镜反转慢到快 |
| CH14 | 0-10 | 无棱镜2 |
|  | 11-255 | 棱镜2切入 |
| CH15 | 0-255 | 保留，无功能 |
| CH16 | 0-255 | 调焦，远到近 |
| CH17 | 0-99 | 无 |
|  | 100-105 | 灯泡关闭，至少保持5S |
|  | 106-199 | 无 |
|  | 200-205 | 灯泡打开，至少保持5S |
|  | 206-255 | 无 |
| CH18 | 0-250 | 无 |
|  | 251-255 | 所有电机复位，至少保持5S |